## Slide 1: Adaptive optics integration at PHELIX
Udo Eisenbarth
THRILL Workshop 16.01.2025

## Slide 2: Phelix in a nutshell
High energy / intensity laser system
1053 nm (Nd:glass)
short pulse: 400 fs, 180 J
long pulse: 10 ns, 1kJ
1 full energy shot / 90 min
3 target chambers
unique combination of high energy laser with heavy ion accelerator

## Slide 3: Wavefront Aberrations
time
wavefront PtV
shot #1
shot #2
shot #3
...Beamlines, Amplifiers...
0
cool down
on-shot
static

## Slide 4: Static Aberrations
Measured at MainAmp output sensor (MAS).
Compensated by deformable mirror at pre-amplifier.
Pre-compensation of MainAmp aberrations.
Measurement / Regulation software: Own development within control system.
Static compensation performed once every morning.
No further compensation over the day (so far).

## Slide 5: On-Shot Aberrations
before shot
on-shot
Main on-shot aberrations are defocus and astigmatism.
Astigmatism compensation
bendable mirror
Defocus compensation
motorized lens

## Slide 6: PHELIX Control System (PCS)
In-house development based on LabVIEW
> 15000 process variables
> 30 PCs in a network cluster
> 100 device classes
  cameras
  energy meters
  motion controllers
  pulsed power
  database
  …
> 350 device instances

## Slide 7: Wavefront Control Integration I
Static wavefront correction
Deformable mirror 1
Deformable mirror 2
Beam quality manager
Actor | Sensor
Def. mirror 1 | MainAmp WF sensor
Def. mirror 2 | Target Chamber WF sensor
MainAmp WF sensor
Target Chamber WF sensor
network
network
Actors and sensors are connected through a routing table.
Communication over control (ethernet) network.
Prepared for controlling not only deformable mirrors but also adaptive groups.
Adaptive Group

## Slide 8: Wavefront Control IntegrAtion II
Pre-compensation of on-shot aberrations
Motorized lenses and bendable mirror have an alignment and 1 (or more) predefined shot positions.
During shot configuration:
  PCS sequencer selects the appropriate shot positions depending on desired setup (e.g. # of amplifier heads to be fired).
Beginning of shot sequence:
  Energy meters are zeroed
  # of averages for wavefront sensors set to 1
  . . .
End of shot sequence:
  Write mesaurement and config data to shot database (PSDB).
  Go back to alignment positions
  # of average back to original value
PCS sequencer

## Slide 9
FURTHER Controls LOOPS: Temporal stabilization
Spectral shift
Spectral shift over delay
Energy Stability
Different paths of pump and signal of ps-OPA: temporal drift  gain fluctuation
Chirped signal + temporal drift: spectral shift
Use spectral shift to stabilize temporal drift

## Slide 10: Future Automations
Currently: two persons / beamtime shift
Goal: One person operation
Automatic setup of laser system depending on desired output beam parameters
  number and gain of amplifiers
  input energy (delivered by frontends)
  diagnostic filter and cam settings
Much more and improved automatic fault detection

## Slide 11
Udo Eisenbarth
GSI Helmholtz centre for heavy ion research
69291 Darmstadt
GERMANY