## Slide 1: Using laser plasma accelerator for simultaneous X-ray absorption and 2-photon Light Induced Fluorescence imaging of a car engine spray
Diego Guénot, Edouard Berrocal, Kristoffer Svendsen, Jonas Björklund Svensson, Martin Hansson, Isabel Gallardo Gonzalez, Henrik Ekerfelt, Anders Persson, Olle Lundh.

## Slide 2: Outline
Spray imaging (what does the title mean?)
Experiment Setup Betatron radiation 2p-LIF
Results and comparison with synchrotron
Conclusion/outlook

## Slide 3: Spray imaging
What is a spray? Systems of droplets immersed in a gaseous continuous phase. Widely used in industry: medicine, painting, cooling, car engines…
Collaboration with Dr. Berrocal from div. Combustion physics (Lund).
Aims at providing the best images of sprays to understand their dynamic
http://www.spray-imaging.com
Spray formation region
Spray region
Large liquid bodies
Primary breakup
Secondary breakup
Spherical
droplets
Liquid core

## Slide 4
Optical techniques
Sprays are highly scattering difficult to image:
Ballistic imaging
Structured Illumination
Light sheet scattering
2 photon Light Induced Fluorescence (2p-LIF)
M. Linne Progress in Energy and Combustion Science 39, 5 (2013)

## Slide 5
Idea: 1) Adding a fluorescent dye in the Spray
2) Exciting the dye with a 2 photon process
Results: remove the scattering before the excitation!
Single-photon fluorescence
Two-photon fluorescence
E. Berrocal et al. continuum, 2, 3 (2019).
2 photons Light Induced fluorescence (2p-LIF)

## Slide 6
2 photons Light Induced fluorescence
Allows for semi-quantitative measurement

## Slide 7
X-ray imaging techniques
Low scattering, tunable absorption:
Phase contrast imaging:
Resolution (few µm)
High speed camera
x Interpretation
Y. Wang et al. Nature Physics, 4 (2008).
M. Linne. Exp Fluids, 52, 1201-1218 (2012).

## Slide 8
X-ray imaging techniques
Low scattering, tunable absorption:
Radiography (< 10keV):
Interpretation: Liquid mass.
x Resolution (50/100µm): Contrast agent.
A. G. Macphee et al Science, 295, 5558 (2002).
LWFA: Simultaneous X-rays and femtosecond laser!

## Slide 9: Experimental setup
Light sheet (10mJ, 50µm x 2cm)
Spray
(water + KI + fluorescine)
Laser (800mJ, 38fs)
Betatron
radiation
X-ray camera
CCD camera + 550nm filter
Gas jet
99% He +1% N2
Vacuum
Air
Al + Kapton
window
Fluorescence
Magnets
Lanex screen
Electrons

## Slide 10
Betatron radiation
At the source: Emax = 2keV, <5.108 photons, >20mrad
Beam transport (80cm): Al (3µm) + Kapton (50µm) + Be (250µm) + air (12cm) Emax = 5.5keV, <5.107 photons
S. Corde et al. Rev. Mod. Phys. 85, 0034–6861 (2013).

## Slide 11
X-ray absorption
100µm of water transmit 80% of the light.
Adding 10% Potassium Iodide (KI) the transmission drops to 60%.
Changes the viscosity by 5% .

## Slide 12
Add 0.1% of fluorecein in the water.
Emit fluorescence around 550nm.
Observation with a long range objective (8µm/pixel).
Quenched by KI .
https://commons.wikimedia.org/wiki/File:Fluorescein_spectra.svg
2 photons Light Induced fluorescence
Excitation 1p
Emission

## Slide 13
Results: simultaneous imaging
Shadowgraphy
6.4mm
8mm
2 mm
Light sheet 2p-LIF
X-ray
The absorption is too weak to distinguish clearly the structures Need to use KI and averaging.
Simultaneous
60µm sensitivity in absorption
2x better than with synchrotron
X-ray (KI)

## Slide 14
Liquid mass dynamic
10
100
200
300
400
Equivalent Path Length [µm]
Average of 50 images
18 times (steps of 50µs and then 100µs)
18mm
8.7mm

## Slide 15
Liquid mass dynamic
t = 150µs
t = 350µs
t = 750µs
10
100
200
300
400
Equivalent Path Length [µm]
Emission of a «sac».
Three large breakup structure.
Steady state: after 500µs.

## Slide 16
Comparison with synchrotron?
https://www.aps.anl.gov/Sector-7/7-BM
https://www.aps.anl.gov/Imaging Halls B. R. Halls et al. Optics express, 25, 2 (2017).
Argonne synchrotron (white beam operation):
5.1010ph (10W), 5µm source size
High rep rate ( video @ 120kHz)
x 5-100keV x Sensitivity of 50µm with 10% KI
Why so high photon energies?
Designed for phase contrast imaging
Too much absorption in windows

## Slide 17
Conclusion and outlook
Conclusion:
Demonstration of the possibility of simultaneous radiography and 2p-LIF imaging of sprays
Improved sensibility compared to synchrotron based measurement
Improvement
x4 Enhanced flux (talk from Vidmantas Tomkus)
Beam transport: reduce distance, thinner Kapton, Al, and Be window.
Future experiments:
High pressure sprays (500bars for GDI or biodiesel)
Swirl sprays, flashball sprays…
Temperature and velocity measurement
D. Guénot et al. Proc. of the 29th European Conf. on Liquid Spray Atomization and Spray Systems (2019).

## Slide 18
Thank you for your attention!

## Slide 19: Annex

## Slide 20
Spray shapes
Shaped-orifice nozzle:
Swirl nozzle (indirect injection):
https://en.wikipedia.org/wiki/Spray_nozzle

## Slide 21
https://ecn.sandia.gov/
The ECN is an international collaboration among experimental and computational researchers in engine combustion, with partners listed below. Our objectives are to:
1. Establish an internet library of well-documented experiments that are appropriate for model validation and the advancement of scientific understanding of combustion at conditions specific to engines.
2. Provide a framework for collaborative comparisons of measured and modeled results.
3. Identify priorities for further experimental and computational research.
Over 50 collaborators (Universities, Bosch, GM, Caterpillar…)
Engine combustion network

## Slide 22
 | LWFA | Synchrotron (APS; 7-BM) (Monochromatic) | Synchrotron (APS; 7-BM) (White beam)
Flux/shot | 108ph | 4.1011ph/s ≈ 3.106ph @ 8keV (±1%) | 10W (max around 10) ≈ 5.1010ph
Energy | 1 to 10keV | 5-15keV | 5-100keV
Source size | 2-3µm | 5*6µm | 80*200µm
Beam divergence | 20mrad | ≈0.1mrad | ≈0.1mrad
Repetition rate | 0.1 Hz (max 1kHz) | 120kHz | 120kHz
Field of view | 22mm (camera) | 4mm | 4mm

## Slide 23: Phase Contrast Setups
Move detector position to disentangle absorption and phase change information
No optics  easy setup, polychromatic source
With assumptions, single-distance measurement
https://en.wikipedia.org/wiki/Phase-contrast_X-ray_imaging
Wilkins, S et al.,Nature. 384 (6607): 335–338 (1996).

## Slide 24: Setup
5 images/angle over
180 degrees in 1 degree increments
 900 images